## Slide 1: The GOES-R Satellite: A New Eye in the Sky

## Slide 2: GOES Satellite “R” series
Under development since late 1990s
Next in progression of GOES satellite series
  Replacing the GOES N/O/P (13/14/15) satellites as they end their scheduled orbital lifespan
ENORMOUS increase of data
  Improvements in spatial, spectral, temporal and radiometric resolution of products
New technology for new products

## Slide 5: Continuity of GOES Operational Satellite Program
Scheduled Launch
January-March 2016

## Slide 6: GOES-R Milestones

## Slide 7: GOES-R Instruments

## Slide 8: Advanced Baseline Imager (ABI)
Improves upon current satellite capabilities
  3 times spectral information
  4 times spatial coverage
  5 times temporal resolution
Continues current products
Allows for new products
  Severe weather forecasting
  Fire and smoke monitoring
  Volcanic Ash Advisories
Visible and Infrared Imagery
  Full Disk every 15 minutes
  CONUS every 5 minutes
  Rapid Scan every minute
  Super Rapid Scan –
    1000 km² every 30 seconds OR 2 areas per minute!
16 Channel imager
  2 visible, 4 near-IR and 10 IR channels

## Slide 14: Progression of GOES Fog Products
Heritage GOES
Fog Detection
GOES-R Algorithm
applied to current GOES
GOES-R Algorithm Applied
to GOES-R **
** Using data from TERRA,
AQUA and GOES, part of
GOES-R Proving Ground

## Slide 16: GOES-R Products
Sample Baseline Products
Aerosols
Clouds and Moisture Imagery
Fire Detection & Characterization (FDC)
Hurricane Intensity Estimation
Hydrology
Snow Cover
Volcanic Ash: Detection & Height
Future Capability Products
Aircraft Icing Threat
Enhanced-V & Overshooting Top Estimation
Flood/Standing Water
Fog/Low Cloud Detection
Turbulence
Visibility
http://www.goes-r.gov/products/ list.html

## Slide 18
www.swpc.noaa.gov

## Slide 19: GOES-R Space Weather
Space Environment In-Situ Suite (SEISS)
  Ensemble of electron, proton and
  heavy ion detection sensors
  Critical information to assess
  electrostatic discharge risk &
  radiation hazard to astronauts
  and satellites
  Warn of high flux events,
  mitigate any damage to radio
  communication
  Data will drive solar radiation
  storm portion of NOAA Space
  Weather Scales
    Geomagnetic storms
    Solar Radiation storms
    Radio Blackouts
www.swpc.noaa.gov/NOAAscales

## Slide 20: GOES-R Space Weather
Extreme UV/X-ray Irradiance Sensor (EXIS)
  Solar X-ray irradiance (XRS) & Solar Extreme UV (EUVS) spectral irradiance in 5-127 nm range
    Issue warnings based on
    solar x-ray increases, large
    spikes from solar flares
    Warnings for radio
    blackouts of terrestrial HF
    radio communications at
    low latitudes
    Potential hazards to
    astronauts in orbit, decrease
    in optimal life of satellites
    (degradation of solar panels)
Current SWPC Irradiance product
New capabilities expected with new
data from GOES-R

## Slide 21: GOES-R Space Weather
Solar UV Imager (SUVI)
  Locates coronal holes, flares and coronal mass ejection source regions
  Characterizes active region complexity
  Improves forecasting of space weather and early warnings of possible Earth environmental impacts
Magnetometer
  Measures time-varying field in magnetosphere
  Provides only operational measure of impact of geomagnetic storms at geosynchronous orbit
  Key in interpreting solar radiation storm measurements by SEISS

## Slide 24
www.goes-r.gov/users/proving-ground

## Slide 28: Formal GOES-R Proving Ground Partners
May 2014

## Slide 30
http://cimss.ssec.wisc.edu/goes_r/proving-ground.html

## Slide 31: NOAA’s Hazardous Weather Testbed
Not just a facility…
…but an organization

## Slide 35: Testbed Takeaways – 2014
Almost ready for operations
  ProbSevere
    Trends on target
    Struggles with mature cells
  NearCast
    Predicted area of convective instability well
    Possibly add an interpolation toggle ability to fill gaps in with NWP
Notes: 35

## Slide 36: Testbed Takeaways – 2014
Get this to my office “yesterday”!
  Lightning Flashes & Lightning Jump Algorithm
    Increases confidence in severity of storms
    Provided information about updraft health
  Super-Rapid Scan Operations (SRSOR) Imagery
    Used to observe key storm-scale features; 1-min temporal resolution made this possible
  Simulated Satellite Imagery
    Comparison to reality raised or lowered confidence in using model
    When on-track, predicted areas of storm development
Notes: 36

## Slide 38: Training and Education Materials
Online Training Modules
How Satellite Observations Impact NWP
GOES-R ABI: Next Generation Satellite Imaging (COMET)
GOES-R: Benefits of Next-Generation Environmental Monitoring (COMET)
Satellite Hydrology and Meteorology for Forecasters (SHyMet)
SPoRT product training modules
VISIT Training Resources
Commerce Learning Center
Printed Materials
GOES-R Fact Sheets (18)
User Readiness Plan
GRB Downlink Specifications and Product Users Guide
Proving Ground Demonstration Final Reports and Annual Reports
New!
Notes: GOES-R: Benefits of Next Generation Environmental Monitoring - Includes an overview of the mission, instruments, system and services, satellite synergy, the role of GOES-R in the Global Observing System as well an environmental monitoring section that addresses the benefits of GOES-R and the ability to monitor 13 unique hazards and phenomena.
GOES-R 101 - Targeted for Forecasters and anyone else interested in basic aspects of GOES-R
Satellite Hydrology and Meteorology (SHyMeT) - Dedicated to operational satellite meteorology. The Forecaster track of the SHyMet course covers satellite imagery interpretation, including feature identification, water vapor channels, and what to expect on GOES-R. There is a session on remote sensing data for operational hydrology as well as one relating to aviation hazards. Other topics include an understanding of the Dvorak method in tropical cyclone analysis and the utility of cloud composites in forecasting
CIMSS Satellite Meteorology for Grades 7-12 -Meteorology is an excellent topic to introduce middle and high school students to geoscience, physics, chemistry, and applied mathematics. Satellite Meteorology provides scientists and educators with exciting tools for investigation, inquiry, analysis and stewardship.
Commerce Learning Center: Forecasters can take these training courses and get credit for taking them

## Slide 39
http://www.goes-r.gov/education/outreach.html
Also Available:
Student Resources
“Fun and Games”